METAR/TAF

NEW AVIATION WEATHER FORMATS

NOTICE:  The following METAR/TAF code formats are undergoing final changes. The proposed effective date is mid 1996, however the date may change.  This handout is for information only.  The information is correct as of June 1, 1995.

INTRODUCTION:  Beginning mid 1996, The United States will convert airport surface observation (SA’s and SP’s) and airport terminal weather forecasts to the International Civil Aviation Organiztion (ICAO) formats.  The surface observations and terminal forecast formats and coding will change.  Other weather products such as winds aloft (FD), area forecast (FA), and pilot reports (PIREPS will begin to incorporate the new weather coding and station identifiers.

The hourly surface observation (SA) will be referred to as METAR (Aviation Routine Weather Report) and the airport terminal forecast will be referred to as TAF (Aerodrome Forecast).  Pilots will notice some differences in the sequence in which information is presented, formatted (e.g. winds and cloud cover), and the abbreviations used.

With little practice and the help of the the help of the tear-out “decoder” card included in this information guide, pilots will find it is easy to understand the new code and will find the additional information in the forecasts (TAF) very useful. Those who use DUATS (Direct User Access Terminal) or commercially provided weather services will find all have included a plain language interpreter just as before.  Flight service briefings will be slightly changed with the sequence of information possibly different and temperature and dew point in degrees celcius.

METAR

Lets check out a METAR

METAR (or SPECI for Special Report) KPIT 201955Z (COR for correction to observation) 22015G25kt   3/4sm   R28R/2600FT   TSRA  OVC010CB   18/16   A2992   RMK   SLP013   T01760158

Note:  When METAR data is missing from the body of the report (e.g. dew point),  it is simply omitted and the user must know the sequence to recognize this.  Some exceptions apply in remarks such as RVRNO, or SLPNO when RVR or SLP are normally reported but not currently available.

To help remember the sequence, think of 3W’s at the beginning----WHERE, WHEN, and WIND. This works for METAR as well is TAF!

METAR  KPIT  201955Z  22015G25KT

WHERE

KPIT  is the ICAO station identifier.  The usual 3 letter identifiers we are all familiar with are now preceded by a “K” for the contigous United States.  Alaska and Hawaii will use 4 letter identifiers beginning with “PA” and “PH” respectively.  Changes are planned to incorporate alphabetic identifiers for those weather reporting stations where numbers and letters are now used (e.g. W10 to HEF).

WHEN

201955Z is the 20th day of the month.

201955Z at 1955Z time

WIND

22015G25KT is reported as the 3 digit direction to the nearest 10 degrees.

22015G25KT  next is the 2 or 3 digit speed

22015G25KT  a “G” comes next if the wind is gusting.

22015G25KT  followed by the 2 or 3 digit maximum speed and units(KT).

00000KT  for calm winds.

20015KT 180v260  When wind direction varies 60 degrees or more and wind is greater than 6 knots.

VRB Used when wind direction is variable and speed is less than or equal to 6 knots.

RMK  Peak wind data shall be reported in the remarks section whenever the maximum instantaneous speed is greater than 25 knots.  22030/15  means a maximum instantaneous wind at 30 knots occurred 15minutes past the hour from 220 degrees.

VISIBILITY

3/4SM  meaning 3/4 statue mile visibility.  Miles and fractions are also reported (e.g.

2 3/4SM for 2 and 3/4 statue miles visibility.

R28R/2600FT  Means Runway Visual Range (RVR). Signifies that the runway visual range for runway 28 RIGHT is 2600 feet.  The format is R (XXX) Runway Designator including (L) left (C)enter or (R)ight /(XXXX) 4 digit visibility in feet.

Some coding pilots may also see for RVR include:

M  indicates that RVR is less than lowest reportable sensor value (e.g. M600FT).

P  indicates RVR greater than highest reportable sensor value (e.g. P6000FT).

V  Variable if the RVR is variable between 2000 and 4000 feet for runway 6L: (R06L/2000V4000FT).

SIGNIFICANT PRESENT WEATHER

TSRA: Thunderstorm/Moderate Rain  Format is a two character descriptor (e.g. TS, SH, DR) followed by a two character weather phenomenon (e.g. RA, SN, FG). (See Abbreviations Section).

CLOUDS

OVC010CB: Specifies cloud amount, height, and type.  Overcast clouds are present at 1000 feet consisting of cumulonimbus clouds.

Cloud height is reported in hundreds of feet.  When clouds are composed of towering cumulus or cumulonimbus TCU or CB will follow cloud height.

The clouds are categorized based on eighths (octas) of the sky:

SKC   Sky Clear

FEW   1-2 octas

SCT     3-4octas

BKN    5-7 octas

OVC    8 octas

VV may be listed here for indefinite ceilingsuch as  “VV004” for Vertical Viibility 400 feet. “VV///”  means indefinte ceiling, height not available.

18/16  Temperature/Dew Point  listed in degrees Celius.  When temperatures are below zero degrees Celius, they are preceded by “M” for Minus (e.g., 10/M06 for temperature 10 degrees C, dew point Minus 6 degrees C).

A2992 altimeter setting “A”  indicates setting in inches of mercury for United States.  Consists of 4 digits: inches and hundreths.

RMK SLP013 T01760158

RMK  SLP013 T01760158. Remarks come last.

RMK SLP013  T01760158. Selected stations will contain SLP for Sea Level pressure reported as the last three digits in hectoPascals (millibars) (e.g., 1013 is reported as SLP013).

RMK SLP013 T01760158.  Also,at selected stations, the 9 character code (T01760158) breaks down the temperature and dew ponit to the nearest 1/10th of a degree Celius. The T stands for for temperature and the “0” means positive temperature. A “1” in the place of “0” stands for negative temperature.  At selected stations, other temperature codes, such as 10142, 20012,  401120084, may appear to document temperatures not related to aviation.

METAR ON ASOS/AWOS

Pilots will notice the METAR/SPECI code and sequence  replaces the format on automated weather observations (AWOS/ASOS). Also when a METAR/SPECI is supplied by an automated source, the notation “AUTO” for automated observation will appear in the report.  The Remarks (RMK) will then contain an abbreviation for the type and number of sensors (A01, A02). If the site is provided by an observer, as in the case of some weather phenomena. The observer’s comments will appear in the RMK section.

An example of a fully automated AWOS/ASOS METAR without human intervention conatins the word AUTO:

METAR KOFP 251955Z AUTO 30008KT  10SM  CLR  22/10  A3010  RMK  AO2  SLP138  T02180096

When AWOS/ASOSreported sky condition is clear (CLR) it means no clouds at or below 12,000 feet.

TAF

Let’s try a TAF

TAF contains a definite forecast for specific time periods and will replace the terminal forecast.

22020KT  3SM  -SHRA  BKN020

FM2030  30015G25KT  3SM  SHRA TAF (TAF AMD is Amended Forecast when included) KPIT 091720Z  091818  OVC015  PROB40  2022  1/2SM  TSRA  OVC008CB

FM2300  27008KT  5SM  -SHRA  BKN020  OVC040 TEMPO  0407  00000KT  1SM  -RA  FG

FM1000  22010KT  5SM  -SHRA OVC020  BECMG  1315  20010KT  P6SM  NSW  SKC

Once you know how to pick out the TAF forecast time periods, the same logical sequence that we saw in METAR will follow.  Below, a TAF is broken down to highlight its individual segments.  Key words, and their definitions, indicating a new period has started are highlighted.

TAF  KPIT  091720Z  091818  22020KT  3SM  -SHRA  BKN020

FM2030 30015G25KT  WS015/30045KT  3SM  SHRA  OVC015 PROB40 2022  1/2SM  TSRA  OVC008CB

FM2300  27008KT  5SM  -SHRA  BKN020  OVC040  TEMPO 0407  00000KT  1SM  -RA  FG

FM1000  22010KT  5SM  -SHRA  OVC020  BECMG  1315  20010KT  P6SM  NSW  SKC

The WHERE, WHEN, AND WIND trick works with TAF, too.  There’s a little twist with the “when”, however.

TAF  KPIT  091720Z  091818  22020KT

WHERE

KPIT  is the ICAO station identifier.  The usual 3 letter identifers we are all familiar with preceded by a “K” for the contigous United States.  Alaska and Hawaii will use 4 letter identifiers beginning with “PA” and “PH” respectively.  Changes are planned to incorporate three letter identifiers for those weather reporting stations where numbers and letters are now used (e.g., W10 to HEF).

WHEN

After KPIT, we see

091720Z  This is the forecast for the 9th day of the month with an issuance time of 1720 Z or UTC.  This is 2 digit date and 4 digit time.

091818 is the valid period with the first two digits containing the day of the month (09).

091818  the econd two digits specify the hour beginning the forecast period (1800Z).

091818  the loast two digits are the hour ending the forecast period (1800Z on the next day, the 10th).

WIND

22020KT

See description under METAR

WS015/30045KT  means at 1500 feet we expect wind to bee 300 degrees at 45 kt.  This indicates low level wind shear, not associated with convective activity.

Time Periods, Etc.

FM2030  From 2030Z or UTC time.  Indicates hours and minutes.

PROB40  2022  There is a 40 percent probability of this condition occurring between 2000Z and 2200Z.

FM2300  From 2300Z.

TEMPO 0407  Temporary changes expected between 0400Z and 0700Z.

FM1000  From 1000Z.

BECMG  1315  Conditions Becoming as described between 1300Z and 1500Z.

Once the specific time periods can be discerned, the sequence of wind, visibilty, significant weather, cloud cover, and cloud height follows and is repeated for each time block.  The only exception is after qualifiers such as PROB40, TEMPO, ans BECMG, some of the components may be omitted if these are not expected to change.  Notice after PROB40 2022, there is no wind given and after TEMPO 0407, there is no cloud cover listed.  TAF’s will also contain wind shear information not associated with convective activity.

It’s BECMG CLR now, isn’t it?

International Differences

Pilots and operators who fly to international destinations are cautioned to be alert to differnces between U.S. METAR/TAF and international METAR/TAF.  Some key differnces follow.

Altimeter setting

The United States reports the altimeter setting in inches of mercury (e.g.,A2992) and internationally it will be reported in hectoPascals (millibars) (e.g., Q1013).

Wind

Internationally wind may be reported in knots (KT), kilometers per hour (KMH) or meters per second (MPS).  Appropriate units are indicated on both METAR and TAF.

Wind Shear

Low level wind shear, not associated with convective activity (e.g., WS015/30045KT, see TAF)  will appear in TAFs in the United Sataes, Canada, and Mexico only.

Visibility

Internationally, visibility is reported in 4 digits using meters with the direction of the lowest visibility sector (e.g., 6000SW - meaning visibility is lowest at 6000 meters to the southwest).  In the United States, we use prevailing visibility, in statue miles, not the lowest visibility, so the same conditions would be reported differently.

International visibility reports also contain a trend such as:

D  Down

U  UP

N  No Change

V  Variable

OTHER

Remarks (RMK) included in U.S. METAR are transmitted to only Canada and Mexico and no other international stations.

Pilots may also see the notation on International METAR/TAF: CAVOK.  This means ceiling and visibility OK and is used to replace weather and clouds if visibilty is 10 kilometers or more, there are no clouds below 1500 meters (5000 feet)  or below the highest minimum air traffic control sector altitude, whichever is greater.  Also, there must be no other significant weather.  NSC means no significant clouds.

International TAFs may include temperature, turbulence, and icing forecasts.

ABBREVIATIONS

A01	Automated Observation without precipitation discriminator (rain/snow)

A02	Automated Observation with precipitation discriminator (rain/snow)

AMD  	Amended Forecast (TAF)

BECMG  Becoming (expected between 2 digit beginning hour and 2 digit ending hour)

BKN	Broken

CLR	Clear at or below 12,000 feet

(AWOS/ASOS report)

COR	Correction to the observation

FEW	1 or 2 Octas (eigths) cloud coverage

FM	From (4 digit beginning time in hours and minutes)

LDG	Landing

M	In temperature field means “minus” or below  zero.

M	In RVR listing indicates visibility less than lowest reportable sensory valus (e.g., M600)

NO	Not available (e.g., SLPNO, RVRNO)

NSW	No significant weather

OVC	Overcast

P	in RVR indicates visbility greater than highest reportable sensor value (P6000FT)

P6SM	Visibility greater than 6 SM (TAF only)

PROB40  Porbability 40 percent

R	Runway (used in RVR measurement)

RMK	Remark

RY/RWY   Runway

SCT	Scattered

SKC	Sky Clear

SLP	Sea Lvel Pressure (e.g., 1013 reported as 013)

SM	Statue mile(s)

SPECI	Special Report

TEMPO   Temporary changes expected (bewteen 2 digit beginning hour and 2 digit ending hour)

TKOF	Takeoff

V	Varies (wind direction and RVR)

VC	Vicinity

VRB	Variable wind direction when speed is less than or equal to 6 knots

VV	Vertical visibilty (Indefinite Ceiling) not associated with convective activity

WS	Wind Shear (in TAFs, low level and not associated with convective activity

Descriptors

BC	Patches

BL	Blowing

DR	Low Drifting

FZ	Supercooled/Freezing

MI	Shallow

PR	Partial

SH	Showers

TS	Thunderstorm

Weather Phenomena

BR	Mist

DS	Dust Storm

DU	Widespread Dust

DZ	Drizzle

FC	Funnel Cloud

+FC	Tornado/Water Spout

FG	Fog

FU	Smoke

GR	Hail

GS	Small Hail/Snow Pellets

HZ	Haze

IC	Ice Crystals

PE	Ice Pellets

PO	Dust/Sand Whirls

PY	Spray

RA	Rain

SA	Sand

SG	Snow Grains

SN	Snow

SQ	Squall

SS	Sandstorm

UP	Unknown Precipitation (Automated 	Observations)

VA	Volcanic Ash

Cloud Types

CB	Cumulonimbus

TCU	Towering Cumulus

METAR (SPECI or Special Report)

Note: When METAR data is missing (e.g., dew point), it is simply omitted and the user must know the sequence to recognize this.  Some exceptions apply in remarks such as RVRNO, or SLPNO when RVR or SLP are normally reported but not currently available.

METAR KPIT 201955Z  22015G25KT  3/4SM  R28R/2600FT  TSRA  OVC010CB  18/16  A2992  RMK  SLP013  T01760158

Where:	KPIT

When:	201955Z  20th day of month at 1955Z

Wind:	22015G25KT  220 degrees at 15 	Gusting to 25 Knots

V:	Variable Direction e.g., 20015KT 	220V280

VRB:	Variable direction when speed is less 	than or equal to 6 knots

Visibility:  3/4SM statue miles, typical

2 3/4SM,1SM

RVR R28R/2600FT  Runway 28 Right Visibility 2600 feet

M:	Used for RVR less than lowest reportable sensor value (e.g., M600FT)

P:	Used for RVR greater than highest reportable sensor valu (e.g., P600FT)

V: 	Variable

Significant Weather:  TRSA  thunderstorm/moderate rain (SEE Abbreviations)

Sky Condition:  OVC010CB overcast clouds at 1000 feet consisting of cumulonimbus

Typical:  SKC,FEW,BKN,VV004  indefinite ceiling (Vertical Visibility) 400 feet or V V/// indefinite ceiling height not available

Temperature/Dew Point:  18/16  18 degrees Celius/dew point 16 degrees Celius

M = Minus (below zero)

Altimeter:  A2992 inches of mercury and preceded by an “A”

RMK SLP013 T01760158  10142  401120084  At selected stations, Sea Level Pressure is reported as the last three digits in hectoPascals (millibars) (e.g., 1013 is reported as SLP013). Codes such as t01760158  10142  20012 and 401120084 are climate temperature information.

TAF (TAF AMD is Amended Forecast  when included).

KPIT  091720Z  091818  22020KT  WS015/30045KT  3SM  -SHRA  BKN 020

FM2030  30015G25KT  3SM  SHRA  OVC015  PROB40  2022  1/2  TSRA  OVC008CB  FM2300  27008KT  5SM  -SHRA  BKN020  OVC040  TEMPO  0407  00000KT  1SM  -RA  FG

FM1000  22010KT  5SM  -SHRA  OVC020  BECMG  1315  20010KT  P6SM  NSW  SKC

Where:	KPIT

When:	091720Z  issuance day and time: 9th 	day at 1720Z / 091818 valid period: 9th 	day at 1800Z to next day (10th) at 	1800Z

Wind:	22020KT  WS015/30045KT  220 	degrees at 20 knots with low level wind 	shear at 1500 feet forecast to be 300 	degrees at 45 knots (only 	nonconvective, low level, wind shear is 	forecast)

Visibility: 3SM  3 statue miles, typical -

2 3/4SM, 1SM /  P6SM : Greater 	   than 6 statue miles

Significant Weather:  -SHRA  light rain showers   (See Abbreviations)

Typical:	FEW, SCT, BKN, OVC.  VV004  indefinite ceiling (Vertical Visibility) 400 feet or VV///.  Indefintie ceiling height not available CB and TCU clouds noted when present.

Sequence of Wind, Visibility, Significant Weather and Sky Conditions repeats preceded by:

FM2030:  From 2030Z

PROB40 2022:  There is a 40 percent probability between 2000Z and 2200Z.

FM2300:   From 2300Z

TEMPO0407:  Temporarily between 0400Z and 0700Z

FM1000:   From 1000Z

BECMG 1315:  Becoming between 1300Z and 1500Z

Note:  Weather conditions such as wind and sky condition may be omitted after PROB40, TEMPO, and BECMG if no change is expected from those same conditions given in the previous time block.